## Slide 1: Ventilator Troubleshooting
Brian Locke, MD
Pulmonary / Critical Care Fellow
University of Utah

## Slide 2: Overview:
You will be faced with one of two problems:
  “The ventilator is alarming”
  “The patient looks uncomfortable” (or, conversely, I gave sedatives to keep them comfortable).
Physiology review: why does this happen?
Schemas for how to address ventilator alarms and patient dyssynchrony

## Slide 3: A warmup riddle:
ABG is 7.15 / 75 / 50 on FiO2 1.0 and PEEP 14, RR 30, Vt 6 ml/Kg
What will stop you from going up on each of these indefinitely?
  Oxygenation = obviously can’t go above pure oxygen.
  What would happen if you kept going up on PEEP? When would you stop?
  What would happen if you kept going fast on RR?
  What would happen if you kept going up on the Vt?

## Slide 4: Part 1: ”The Ventilator is Alarming”
What is the alarm?
  Circuit disconnect, Breath not Delivered
    Inspect circuit for break or kink
  Minute ventilation low?
    Are you on pressure support? Put on assist control-mode
    Are you in ACPC? This is the equivalent of high pressures
  Minute ventilation high?
    Is this rapid shallow breathing? Go to patient looks uncomfortable
  Large Tidal Volume?
    Is this breath stacking? Discuss in 2nd part
  Most common: High peak pressures pressures

## Slide 5: Why is this so hard? 2 conflicting principles of ventilator management
Lung Protective Ventilation: ARMA, 2000
  Sedate deeply, unnaturally small breaths to protect lung
Notes: Baby lung = the injured lung is nonfunctional, breaths are going to a small remaining part of the lung.
Spectrum from deeply sedated, very protective breathing to very awake, breathing how our brainstem wants = injurious

## Slide 6
Notes: Tobin
N Engl J Med 2001; 344:1986-1996 DOI: 10.1056/NEJM200106283442606

## Slide 7: Why is this so hard? 2 conflicting EBM principles of critical care
Daily sedation vacation
  Restart at ½ dose; avoid accumulation
Less sedation accumulation, faster weaning and extubation
Notes: ABC / Wake up and breath paired this with SBT -> probable mortality benefit (Lancet, Giroud)
These are in conflict: deeper sedation allows safer ventilation, but light sedation shortens time on the vent and also helps mortality

## Slide 8: Why is this so hard? 2 conflicting EBM principles of critical care
Lung Protective Vent
Brainstem desired Vent
Deeply Sedated
Lightly Sedated
Priorities shift:
  Early in course: most inflamed lungs. Prioritize left
  Later in course: weaning crucial. Prioritize right
Ventilator Alarms = how to ensure Lung Protective Vent occurring
Patient synchrony = how to do Lung Protective Vent with least sedation
Ideal
Ideal
Notes: Thus, the goal of part 1: how can we make sure our ventilation is afe?
The goal of part 2: how can we have the sedation as light as possible but still allow safe ventilation.
Priorities shift throughout duration of illness: sometimes you have to sacrifice one for the other.
  First day = most important to safely ventilate (most inflamed lungs), first week more important than next. Etc.
  As they get closer to extubation, more awake is more important. Thus, balance my shift from day to tday.

## Slide 9
Assisted vs Control Breath
What the patient is getting
Ventilator Mode Setting
How the ventilator is set
Bump to 100% FiO2 for 2 minutes
Stop the honking
End-Inspiratory Hold
Alarm shows up here (Yellow or Red, based on urgency)

## Slide 10: Modes:
Notes: Assist Control / Volume Control (ACVC):
  You set the tidal volume, the inspiratory time: then the stiffness of the lungs determines how high the pressure must go to achieve that
  KEY POINT: the PRESSURE is the dependent variable
Assist Control / Pressure Control (ACPC):
  You set the inspiratory pressure, the inspiratory time: then the stiffness of the lungs determines how much volume results
  KEY POINT: the VOLUME is the dependent variable
  Start with ACVC, can talk about ACPC if time and interest allow.
  ***think about how this all would be different in ACPC as we go

## Slide 11: There are things we set and variables that result from the patient’s physiology
In AC/VC Mode:
  We set how the breath is given: Tidal Volume, Inspiratory Time/Flow Rate
  The stiffness & airflow resistance of the lungs determine how much pressure required to achieve set Vt
  The resistance to airflow determines how fast the breath comes back
Notes: Assist Control / Volume Control:
  You set the tidal volume, the inspiratory time: then the stiffness of the lungs determines how high the pressure must go to achieve that
  KEY POINT: the PRESSURE is the dependent variable

## Slide 12: “The peak pressures are high”
Pressure measured at the ventilator
Measured pressure = sum of two components
  1: Resistance to flow (the pressure you feel blowing through a straw)
  2. Distending pressure to inflate the alveoli + chest wall (the pressure you feel blowing a balloon up)
Resistive pressure depends on flow rate!
Distending Pressure
Resistive Pressure
Pressure measured here
Notes: How can you separate what pressure is coming from air movement, and what is coming from alveoli inflation?

## Slide 13: Breath holds:
Flow = 0, then the resistive component = 0. Left with only the static component.
  End-inspiratory hold = measures the plateau pressure (= the pressure with the alveoli full)
  End-expiratory hold = measures the PEEP (= the pressure when the alveoli is deflated)
Resistive
Distending

## Slide 14: Two examples:
Peak = 55 cmH2O.
Plateau = 40 cmH2O
Why is the pressure high?
Peak = 55 cmH2O.
Plateau = 15 cmH2O
Why is the pressure high?

## Slide 15: Which do you care about?
Volutrauma and Barotrauma result from elevated transpulmonary pressure (=static pressure difference between the alveoli and the pleural pressure)
  LTVV = we want to keep the plateau less than 30 CMH2O
What things cause an increase in plateau pressure?
Distending Pressure
Resistive Pressure
Pressure measured here

## Slide 16: Elevated plateau pressure
Stiff lungs (ARDS, pneumonia, pretty much any infiltrate)
Water-logged lungs (worsening edema)
Over-distending the alveoli
  Tidal volume is too big
  Ventilating only a single lung (Pneumothorax, main-stem intubation)
External compression (effusion, chest wall, abdomen)
PEEP…
  Intrinsic PEEP aka ‘auto-PEEP’, air trapping
  Extrinsic PEEP

## Slide 17: PEEP increased by 4 cmH2O… how much should the plateau go up?
  If you recruit lung: by less than 4 cmH2O
  If you over-distend alveoli, by less than 4 cmH2O
  If both the above don’t change, it’ll go up by 4 cmH2O
0 mmHg
Driving Pressure
Notes: Plateau pressure = PEEPintrinsic + PEEPextrinsic + Driving Pressure
  Driving pressure = the amount of pressure it takes to open the lung to the volume you’re getting.
  The only way to know is to try it.

## Slide 18: What if peak is high, plateau is low?
Problems with flow
  Bronchospasm
  Mucus plug
  Kink in the ventilator tubing or ETT
  Giving breaths with very fast rate
What is the consequence of a high peak pressure if the plateau is low?
  NOTHING

## Slide 19: Then why are the RN’s always coming to me with the peak pressure?
You can’t accurately measure an accurate end-inspiratory hold if the patient is making inspiratory efforts
  If deeply sedated or paralyzed, will be accurate.
Distending Pressure
Resistive Pressure
Pressure measured here
Muscular Effort
P
Notes:   Often, we follow the peak pressures IF we are confident that the flow resistance hasn’t changed.
  If you can make some guesses based on the Flow-Volum loops, but this is advanced.
    If you really can’t figure it out, sometimes you need to sedate the patient to get this info

## Slide 20
Expiratory hold maneuver
Giving breath too fast
Notes: Can you get an accurate plateau pressure? If so, do it
  If Plat is also high: (static pressure problem)
    CXR (PTX, edema, worsening ARDS),
    US for pneumothorax/effusion,
    titrate the PEEP down if you can
    Drop the Vt if you can
  If plateau is not high: (flow pressure problem)
    Make sure there is no kink in the tubing
    Suction out goobers
    Give bronchodilators.
    Slow the speed the breath is given
If you can’t get a plateau pressure – try some things from both, consider sedation if you really need to know.

## Slide 21: In sum,
In ACVC, Tidal Volume and Inspiratory time are set, so pressure will vary based on the patient’s lung physiology
Ventilator pressures (specifically, the plateau pressure) tell you about whether current ventilation is lung protective
Tradeoff between Lung Protection (early) vs Light Sedation (late)
High peak pressure will be the finding nurses and RTs notice
  How will this change in ACPC? (answer at end)
Perform a breath hold (if you can) to separate causes of elevated resistance to flow (low plateau) vs high distending pressure (high plateau)
Notes: Note: After giving this presentation, this article and presentation came out in CCM – gives some doubt to sedation dichotomy
Article - https://journals.lww.com/ccmjournal/fulltext/2021/12000/discordance_between_respiratory_drive_and_sedation.9.aspx
Editorial - https://journals.lww.com/ccmjournal/fulltext/2021/12000/managing_patient_ventilator_dyssynchrony_.18.aspx
Their summary of the traditional management:
Patient factors that affect the respiratory drive are complex (3). The normal respiratory pattern generator is in the brain stem and is affected by chemical stimuli (especially pH and to a lesser extent Po2 and Pco2), mechanical inputs from the lungs and thoracic cage (especially stretch receptors), and the cerebral cortex (voluntary activity, anxiety, pain reflexes). Disease states can profoundly affect this system both directly (i.e., systemic or specific CNS inflammation) or indirectly through effects on metabolism, respiratory system mechanics, anxiety/stress, and pain. All of these effects should be addressed and managed with appropriate clinical strategies.
When optimal clinical management has not achieved a reasonable level of patient-ventilator synchrony, the next option is pharmacologic blunting of the respiratory drive (4). Three classes of agents are generally employed to accomplish this: opioids, sedatives, and neuromuscular blockers (NMBs). Opioids are effective pain control agents and can both decrease pain inputs into the respiratory control center as well as directly slow the respiratory rate. Sedatives include a broad range of specific agents that reduce stress/anxiety inputs as well as directly suppress the respiratory control center to varying degrees. Both of these drug classes also can have profound effects on general levels of consciousness, hemodyanamic function, and long-term mental status (e.g., prolonged delirium after certain sedative agents). The final drug option is NMB, an option usually reserved for uncontrolled PVD by other means. NMBs can effectively eliminate respiratory muscle activity but offer no pain or anxiety control and are associated with muscle disuse atrophy and long-term myopathy. A theoretical way to mitigate this risk is to consider NMB dosing strategies that blunt neuromuscular transmission but does not completely ablate it (“NMB lite”).

## Slide 22: ”The patient looks uncomfortable”
“Or, I had to go up on the sedation”
Observation (confounded) data suggests:
  25% of all patients have dis-synchrony
  50% who are the vent more than a day will.
  They do worse. Maybe even worse mortality

## Slide 23: Double Triggering -> Breath Stacking
Two breaths are given for the patient making one respiratory effort
This is a problem because it doubles the distention of the lung
Cause: the patient’s brain stem wants a larger/longer inspiration than the vent gives.
  Low Tidal Volume = unnatural
  Drive to breath = high

## Slide 24: Double Triggering -> Breath Stacking
Treatment options:
  Increase sedation (often preferrable if early = strict low tidal volume ventilation needed)
    Neuromuscular blockade if needed
  Increase vent inspiratory time
  increase tidal volume (often preferrable if later = lighter sedation prioritized.
Notes: Two breaths are given for the patient making one respiratory effort
This is a problem because it’s equivalent to 12 ml/Kg of distention in the lung.

## Slide 25: Flow starvation -> wasted effort
Cause
  Patient wants more flow than the vent gives (common on ACVC)
Consequence:
  Skeletal muscle and diaphragm strain
  Lung injury (pleural pressure negative during efforts)

## Slide 26: Flow starvation -> wasted effort
Treatment Options:
  Increase the flow rate to 50-60, can increase up to 80.
    This will cause peak pressure to go up
  Switch to ramp waveform
  Switch to ACPC

## Slide 27: A warmup riddle: answers
ABG is 7.15 / 75 / 50 on FiO2 1.0 an PEEP 14, RR 30, Vt 6 ml/Kg
What will stop you from going up on each of these indefinitely?
  Oxygenation = obviously can’t go above pure oxygen.
  What would happen if you kept going up on PEEP? When would you stop?
    Plateau is likely to increase above 30 cmH2O
  What would happen if you kept going fast on RR?
    AutoPEEP due to insufficient time to exhale
  What would happen if you kept going up on the Vt?
    Plateau is likely to increase above 30 cmH2O
What will the RNs/RTs come to you with in ACPC instead of high peak pressure?
  “Tidal volume [or Minute Ventilation] is low”. Can still check plat / do all the same troubleshooting

## Slide 28: Questions?
brian.locke@hsc.utah.edu